## Slide 1: (1/8) Million-Module March: Scalable Locomotion for Large S-R Robots
Robert Fitch
National ICT Australia
Zack Butler
Rochester Inst of Tech
August 19, 2006

## Slide 2: Scalability Challenges in S-R
Useful systems will probably need thousands of modules
Each module may need to be simple
Can’t use linear space per module or linear time per action
  Essentially precludes exact shapes?
  Locomotion algos can use minimal space, but are restricted in operation

## Slide 3: One Million (Point) Modules

## Slide 4: Proposed Approach
Simplified shapes for planning
Parallel path planning via MDP-inspired dynamic programming
Safe parallel actuation via local connectivity checks
Efficiency depends on shape
  This may be true for many techniques

## Slide 5: Example: Large (22^3) Robot Among Obstacles

## Slide 6: Sublinear Planning
Sublinear in time and space
Bounding box to describe goal
  Could be arbitrarily more complex
Each module not in goal finds a path to closest goal location
  Formulated as MDP
  Plans are continuously updated as each module moves
  Assuming SlidingCube abstraction, although not limited to this

## Slide 7: MDP Formulation – GridWorld Example

## Slide 8: MDP Formulation
States S: all module locations (current & potential)
Actions A: module motions (6 faces x 4 moves + null = 25)
Reward r = -1 (not in goal), or -k*height (in goal)
Policy is therefore a legal motion for each location such that each module finds a goal in minimum time
No attempt to assign goals to modules
  Not all goal locations reachable anyway

## Slide 9: MDP Implementation
Each module keeps track of adjacent locations
Assume bounding box overlaps robot
Best policies are propagated from goal
Module motions trigger updates

## Slide 10: MDP Implementation
Bounding box can overlap any obstacle
  Even insufficient size is OK
  Moving bounding box produces locomotion

## Slide 11: Parallel Actuation
Must prevent global disconnection
  Check for articulation points
  Heuristic search ensures all neighbors remain connected after motion (find connecting cycle)
  Iterative deepening limits search time
Must avoid collisions
  Lock modules in connecting cycle
  Test-and-set destination position
  Move
  Free locked modules
?

## Slide 12: Parallel Actuation
Modules search locally & move in parallel

## Slide 13: Efficiency Issues
Technique works best for blobby shapes
  Modules multiply connected, many can move at once, bounding boxes for goals
But gracefully degrades as well
  Dynamic program runs in O(d) time
    d = diameter, can be up to n
  Neighbor connectivity search also will find shortest paths but as long as required

## Slide 14: Philosophical Points
Algorithms (for the same task) have different requirements/capabilities
Important to consider task requirements
  Shape fidelity, shape geometry, heterogeneity, speed of reconfiguration
As well as (traditional) module issues
  Memory, relative speed of communication and actuation, etc.

## Slide 15: End

## Slide 16: Example: Single Obstacle

## Slide 17: Example: 1000 Modules with Obstacles