## Slide 1: On Scalability Issues in Reinforcement Learning for Modular Robots
Paulina Varshavskaya, Leslie Pack Kaelbling and Daniela Rus

## Slide 2
motivate reinforcement learning (RL)
larger modular system challenges
a specific solution
a general solution
experiments in simulation
related current work

## Slide 3: RL for self-reconfigurable robots
1. automated controller design
Butler et al 2000
MTRAN-II controller: genetic algorithms (Kamimura et al 2004)
Molecube controller: genetic algorithms (Mytilinaios et al 2004)
Telecube primitives and controller: genetic programming (Kubica and Rieffel 2002)

## Slide 4: RL for self-reconfigurable robots
2. online adaptation
moving from 1. to 2.
from the point of view of each robot or module
limited knowledge and resources
1. automated controller design

## Slide 5: Task: locomotion in modular robots
Molecule Kotay & Rus 2005
x4
lattice-based robots
simulated generalized lattice-based robot

## Slide 6: From each agent’s point of view
local observation: Moore neighborhood
x
actions: 8 directions + NOP
reward: Eastward displacement along x axis
- acting module
- neighbor present
- empty lattice cell
assumptions: primitive “physics”, no disconnections,
failed actions don’t execute, synchronous execution
state: global configuration of robot
unknown

## Slide 7: Large modular sytem challenges
partial observability
large observation-action spaces
28 observations without obstacles x 9 actions
38 observations with obstacles x 9 actions
cannot use Markov-assuming “nice” algorithms

## Slide 8: Partial observability
direct policy search using gradient ascent in policy space (GAPS)
Peshkin 2001
Value V(θ) of policy π(θ)
value of
in a multi-agent partially observable Markov Decision Process (POMDP)

## Slide 9: GAPS
each agent executes
a parameterized policy
at time t:
observe ot
select at according to policy
execute at
receive reward rt
keep an execution trace
at end of episode:
update parameters θ
ot
at
Rt
θ
βt is “temperature”

## Slide 10: Large modular sytem challenges
partial observability
large observation-action spaces
28 observations without obstacles 2,304 parameters
38 observations with obstacles 59,049 parameters
x
- acting module
- neighbor present
- empty lattice cell

## Slide 11: Specific solution: incremental learning
x 2
x 4
x 8
x 4
x 4
x 8
x 8
x 4
x 2
x 2
= 36
=162
= 414
possible observations
x 9 possible actions = total number of parameters
2 modules
3 modules
4 modules
9+ modules
= 2,304
- acting module
- neighbor present
- empty lattice cell

## Slide 12: Incremental GAPS (IGAPS) performance
Varshavskaya et al 2004
Mean convergence times comparison
Mean average reward comparison

## Slide 13: A specific solution
additive nature of modular robots
unclear applicability to other tasks and systems
faster RL but not fast enough for online adaptation

## Slide 14
Desirable general solution
x 2
x 4
x 8
x 4
x 4
x 8
x 8
x 4
x 2
x 2
possible observations
total number of parameters
2 modules
3 modules
4 modules
9+ modules
small n
small n
small n
small n
- acting module
- neighbor present
- empty lattice cell

## Slide 15
Features
φ7 =
φ88 =
1 if upper left corner full & a=NE
0 otherwise
1 if upper right corner empty & a=SE
0 otherwise
φ45 =
φ75 =
1 if empty row in front & a=SE
0 otherwise
1 if upper left corner empty & a=W
0 otherwise
– acting module
– neighbor present
– empty space
– don’t care

## Slide 16
Approximation by feature spaces
define a number of feature functions
over the observation-action space
policy computed from the dot product of
the feature vector and parameters θ
a few features approximate the desired space
learning with a modified log-linear GAPS (LLGAPS)

## Slide 17
Full feature set
1
-
9
1
-
9
1
-
9
1
-
9
144 features
– acting module
– neighbor present
– empty space
– don’t care
observation
observation
observation
observation
action
action
action
action
1
-
9
1
-
9
1
-
9
1
-
9
1
-
9
1
-
9
1
-
9
1
-
9
1
-
9
1
-
9
1
-
9
1
-
9

## Slide 18: Performance comparison
reward
Performance as learning progresses:
Smoothed average reward over 10 runs
Mean convergence times comparison

## Slide 19: Learned locomotion

## Slide 20: Summary so far
reinforcement learning for modular robots with more realistic observability assumptions
learning algorithm with feature representation
results in locomotion by self-reconfiguration

## Slide 21: Advantages of a feature representation
faster learning
number of parameters independent of robot size or observation space size
domain knowledge
  “don’t try to move into an occupied cell”
features can be designed for many tasks and robots

## Slide 22: Current work: asynchronous execution
24 observations, 11 actions
only 220 features
reward

## Slide 23: Current work: large system locomotion
20 modules
70 modules

## Slide 24: Current work: complex reward
θ1
θ2
θn
ot
arbitration
at
world
r1
rn
distribute subtasks within each module

## Slide 25: Current work: locomotion in truss robots
Shady Vona et al 2006
x4
MultiShadySim Detweiler et al 2006

## Slide 26
Questions?
project sponsored by Boeing Corporation